## Slide 1: Dr. Yonis. M. Yonis Buswig
Electrical Safety

## Slide 2: Electrical Hazards
To avoid injuries, you should be aware of electrical hazards. Some of the most common electrical hazards are:
Exposed electrical parts
Overloaded circuits
Defective insulation
Improper grounding
Damaged power tools
Overhead power lines
Wet conditions
Let’s take a closer look at each of these hazards.
www.CareerSafeOnline.com

## Slide 3: Exposed Electrical Parts
Exposed electrical parts can include:
Breaker boxes without a cover
Electrical terminals in motors, appliances, and electronic equipment
www.CareerSafeOnline.com

## Slide 4: Overloaded Circuits
Overloading a circuit increases the potential for fires to occur. Overload hazards exist if:
www.CareerSafeOnline.com
•
Too many devices are plugged into a circuit
The wire insulation melts
An improper overcurrent protection device is used
No overcurrent protection device is used

## Slide 5: Overloaded Circuits
Overcurrent protection devices include:
Circuit breakers
Fuses
Ground fault circuit interrupters (GFCI)
A circuit breaker automatically “trips” and shuts off the current in a circuit if it becomes overloaded.
www.CareerSafeOnline.com

## Slide 6: Overloaded Circuits
A fuse contains an internal part that melts and shuts off the current if there is an overload.
Circuit breakers
Fuses
Ground fault circuit interrupters
www.CareerSafeOnline.com

## Slide 7: Overloaded Circuits
A ground fault circuit interrupter (GFCI) detects current leaking from a circuit to ground and shuts the current off.
Circuit breakers
Fuses
Ground fault circuit interrupters
Receptacle type
www.CareerSafeOnline.com

## Slide 8: Defective Insulation
To protect you, electrical wires are insulated by a plastic or rubber covering. Insulation prevents conductors from coming in contact with each other and with people.
Make sure the insulation of tools and cords you are using is not damaged.
www.CareerSafeOnline.com

## Slide 9: Grounding
When an electrical system is properly grounded, there is a path that allows the current to travel to the earth (the ground).
When any electrical system is not properly grounded, a hazard exists.
www.CareerSafeOnline.com

## Slide 10: Power Tools
Power tools that are damaged or not properly maintained can cause you to be seriously injured.
If you touch a metallic part of a power tool that is energized because of damaged insulation or improper grounding, you could be shocked.
www.CareerSafeOnline.com

## Slide 11: Power Tools
To protect you from shock, burns and electrocution, tools must:
Have a three-wire cord with ground and be plugged into a grounded receptacle.
Be double insulated.
Be powered by a low-voltage
isolation transformer.
www.CareerSafeOnline.com

## Slide 12
Overhead Power Lines
Overhead power lines are not usually insulated, and cause more than half of all electrocutions.
www.CareerSafeOnline.com

## Slide 13: Wet Conditions
Wet conditions are hazardous because you can become an easy path for electrical current.
There are many circumstances that create wet conditions:
Standing in water
Wet clothing
High humidity
Perspiration
www.CareerSafeOnline.com

## Slide 14: Safe Work Practices
•
Inspect cords before each use
Never overload a circuit
Stay away from all unguarded conductors
To unplug, pull on the plug, not the cord
Don’t wear jewelry or use other metal objects around electrical
equipment
You can StartSafe and StaySafe by using the following safe work practices:
www.CareerSafeOnline.com

## Slide 15: Safe Work Practices: Training
Training concerning electricity is very important. Training for employees working with electrical equipment must include how to:
•
De-energize the equipment
Use lockout and tag procedures
Use insulating protective equipment
Maintain a safe distance from energized parts
Use appropriate PPE
www.CareerSafeOnline.com

## Slide 16: Safe Work Practices: Lockout/Tagout
When performing lockout/tagout on circuits, trained employees will do the following:
Turn off the power supply
Put a lock on all power sources to the circuit
Apply a tag
Test the circuit
www.CareerSafeOnline.com

## Slide 17: Summary
It is very important to StartSafe and StaySafe around electricity. In order to do so:
Know the hazards
Plan your work and plan for safety
Avoid wet working conditions and other dangers
Avoid overhead power lines
Use proper wiring and connectors
Use and maintain tools properly
Wear the correct PPE for the job
www.CareerSafeOnline.com

## Slide 18: Electrical Safety in the Laboratory